Aircraft Maintenance

Maintenance means the preservation, inspection, overhaul, and repair of aircraft, including the replacement of parts.  A PROPERLY MAINTAINED AIRCRAFT IS A SAFE AIRCRAFT.

The purpose of maintenance is to ensure that the aircraft remains airworthy throughout is operational life.

Although maintenance requirements will vary for different types of aircraft, experience shows that most aircraft will need some type of preventative maintenance every 25 hours or less of flying time, and minor maintenance at least every 100 hours.  This is influenced by the kind of operation, climatic conditions, storage facilities, age, and construction of the aircraft.

Inspections

FAR Part 91 places primary responsibility on the owner or operator for maintaining an aircraft in an airworthy condition.  Certain inspections must be performed on the aircraft, and you must maintain the airworthiness of the aircraft between required inspections by having any defects corrected.

FAR’s require the inspection of all civil aircraft at specific intervals to determine the overall condition.  The interval depends generally upon the type of operations in which the aircraft is engaged.  Some aircraft need to be inspected at least once each 12 calendar months, while inspection for others after each 100 hours of operation.  In other instances, an aircraft may be inspected in accordance with an inspection system set up to provide for total inspection of the aircraft on the basis of calendar time, time in service, number of system operations, or any combination of these.

Annual Inspection

Any reciprocating-engine powered or single-engine turbojet / turbopropeller driven small aircraft (12,500 or under) flown for pleasure is required to be inspected at least annually by an FAA certificated A & P mechanic holding an Inspection Authorization, or an FAA certificated repair station that is appropriately rated, or the manufacturer of the aircraft.  The aircraft may not be operated unless the annual inspection has been performed within the preceding 12 calendar months.  A period of 12 calendar months extends from any day of a month to the last day of the same month the following year.  However, an with the annual inspection overdue may be operated under a special flight permit issued by the FAA for the purpose of flying the aircraft to a location where the annual inspection can be performed.

100 Hour Inspection

Any reciprocating-engine powered or single-engine turbojet/turbopropeller driven small aircraft used to carry passengers or for flight instruction for hire, must be inspected within each 100 hours of time in service by an FAA certificated A & P mechanic, an FAA certificated repair station that is appropriately rated, or the aircraft manufacturer.  An annual inspection is acceptable as a 100 hour inspection, but the reverse is not true.

Progressive Inspection

UND maintains and inspects its PA-28R-201 fleet (Piper Arrows) under a Progressive Inspection Program. FAR 91.409 outlines the requirements for establishing and maintaining a progressive inspection program

Personnel and Facilities 
The progressive inspection will be performed by a certified mechanic holding Inspection Authorization (IA), or by a certified repair station as explained in FAR 91.409 (d). UND's maintenance shop is a certified repair station.

Phase Inspections 
Instead of performing the annual or 100 hour inspection all at once, UND breaks the inspections into four phases. Each phase inspection includes a detailed inspection of select components and a routine inspection of the remaining components. Phase inspections are conducted at 60 hour intervals. After all four inspections are complete, the aircraft has undergone the equivalent of an annual inspection.

FAR 91.409 states that the aircraft must be airworthy at all times, and that the program must ensure that a complete inspection (detailed inspection of all components, completing an annual) is completed within each 12 calendar months. To comply with this FAR, the four phase inspections must be completed within a 12 month period.

The following table breaks down each phase inspection:

| Phase | Detailed Inspection Items | Routine Inspection Items |
| --- | --- | --- |
| 1 | Fuselage, Cabin, Empennage | Engine, Propeller, Wings, Landing Gear |
| 2 | Engine, Propeller | Cabin, Fuselage, Empennage, Wings, Landing Gear |
| 3 | Wings, Landing Gear | Cabin, Fuselage, Empennage, Engine, Propeller |
| 4 | Engine, Propeller | Cabin, Fuselage, Empennage, Wings, Landing Gear |

Equipment Inspections

Transponder

No person may use an ATC transponder unless within the preceding 24 calendar months, the transponder has been tested and inspected.  This is according to FAR 91.413.

Emergency Locator Transmitter

ELT’s must be inspected within the preceding 12 calendar months after the last inspection for:

- Proper installation

- Battery corrosion

- Operation of the controls and crash sensor

- The presence of a sufficient signal radiated from its antenna

This is in accordance with FAR 91.207

Pitot-Static

The pitot-static system must be inspected every 24 calendar months before IFR flight in controlled airspace.  This is in accordance with FAR 91.411

Sample Phase One Inspection

PROGRESSIVE INSPECTION GUIDE

PIPER

PA28-161

PA28R-201

INSPECTION NO. 1

DETAILED INSPECTION ITEMS---FUSELAGE, CABIN AND EMPENNAGE

ROUTINE INSPECTION ITEMS--ENGINE, PROPELLER, WINGS AND LANDING GEAR

N					W/O#					TACH

PRE RUN-UP INSPECTION						      INSP.

1.	Inspect for excessive fuel or oil leakage.	_________________

If required, thoroughly wash aircraft prior to run-up.

2.	Aircraft Records - check FAA approved Owners 	_________________

Manual for completeness and current revisions.

Check airworthiness certificate and registration certificate.

3.	SB's and AD's - check status of current Service	_________________

Bulletins and Airworthiness Directives.

4.	Time Life Items - check status of Time Life Items.	_________________

______________________________________________________________________________

PRE INSPECTION RUN-UP

1.	Brakes

2. 	Starter

3.	Engine Instr.

4. 	Alt. Output

5. 	Avionics Oper.

6. 	Ammeter

7. 	Magneto-175 Max, 50

Diff at 2000 RPM Max

10 sec. each mag.

8.	Carb Heat Check

9. 	Propeller Check at 1500

RPM, 500 RPM decrease

(201 only(

10. 	Power Check (Max 2 min. or 475 F with cowling removed(

11. 	Heat and Vent  Systems

12. 	Fuel Gauges

13. 	Boost Pump

14. 	Fuel Selector

15. 	All Lights

16. 	Elec. Trim Oper.

17. 	Flaps

18.	Pitot Heat 			     19. 	Instruments

20.	Standby Vacuum System

21.	Idle RPM, 550-650 RPM

22.	Idle cut-off

23.	Magneto Safety Check

DETAILED INSPECTION ITEMS---FUSELAGE, CABIN AND EMPENNAGE

FUSELAGE									      INSP.

1.	Fuselage Surface - inspect for skin damage, loose rivets,	__________________

condition of paint, and check pitot-static ports and

drain holes for obstruction.  Inspect fuselage scupper

drains for obstruction.

2.	Step  - inspect fixed step for condition and security.	__________________

3.	Internal Fuselage Structure - inspect bulkheads	__________________

door posts, stringers, doublers, and skins for

corrosion, cracks, buckles, and loose rivets,

bolts, and nuts.

4.	Wing Attach Brackets - inspect fittings, brackets	__________________

and bolts for condition and security.

5.	Electrical Wiring - inspect for proper routing,	__________________

support, security of terminal connections, and

condition of insulation.

6.	Avionics - inspect equipment for security, condition	__________________

and proper installation.

7.	Hoses, Metal Lines, and Fittings - inspect for condition	__________________

leakage, proper routing, and support.

8.	Fuselage Mounted Optional Equipment - check autopilot	__________________

and flight director equipment for general condition

security of attachment.

9.	Antennas and Cables - inspect for security of attachment	__________________

connection, and condition.

10. Placards and Data Plates - check for presence and	__________________

legibility.

11. Hydraulic Power Pack (201 only) - inspect pack and	__________________

lines for damage, leaks, and security.  Check power

pack fluid level.

12. Battery - remove, inspect battery for condition, and proper	__________________

fluid level.  Clean battery and charge.  Inspect battery box

for corrosion and security of attachment.

FUSELAGE	    INSP.

13. Electrical Wiring - check electrical wiring, connections	__________________

and solenoids for condition and security.

_____________________________________________________________________________

CABIN	    INSP.

1.	Lighting - check operation, condition of lens,	__________________

and security of attachment of instruments, cabin

and avionics lighting.

2.	Switches and Circuit Breakers - check operation of switches	__________________

and condition and markings of circuit breakers.

3.	Stall Warning System - check operation and 	__________________

adjustment of stall warning system.

4.	Instruments - check general condition and markings	__________________

for legibility.

5.	Instrument Panel - inspect shock mounts, ground straps	__________________

and covers for deterioration, cracks, and security of

attachments.

6.	Instrument Lines, Fitting, Ducting, and Instrument	__________________

Panel Wiring - check for proper routing, support,

and security of attachments.

7.	Flight Controls - check cable, push-pull rods, bellcranks	__________________

pulleys, turnbuckles for condition, security, and

operation.

8.	Control Column - inspect pulleys, sprockets, bearings, 	__________________

chains, and turnbuckles for condition, security, and

operation.

9.	Control Wheel - check general condition and operation.	__________________

10. Flight Control Travel Check - check freedom of movement	__________________

and proper operation through full travel with and without

flaps extended.

CABIN	    INSP.

11. Wing Flap Control - check operation through full travel	__________________

and observe Flap position and Detents.  Check condition of

springs, cable, and cable attachment.

12. Trim Controls and Indicator - check freedom of movement	__________________

and proper operation through full travel.  Check pulleys,

cables, sprockets, bearing chains, and turnbuckles for

condition and security.

13. Rudder Pedals and Linkage - check for general condition, 	__________________

proper rigging, and operation.  Check for security

of attachment.

14. Brakes, Master Cylinders, and Parking Brake -  check master	__________________

cylinders and parking brake mechanism for condition and

security.  Check fluid level and test operation.

15. Fuel Selector Valve - check controls for detent in each position,	__________________

security of attachment, operation of off lock, and proper placarding.

16. Seats, Seat Belts, and Shoulder Harnesses - check seat	__________________

structure, slides, seat stops, and adjustment mechanism

for condition, operation, and security of attachment.

Inspect belts for condition and security of fasteners.

17. Engine Controls and Cabin Comfort Controls - check	__________________

freedom of movement through full travel.  Check

friction locks for proper operation.

18. Ventilating System - check all fresh air and heat	__________________

outlet vents for proper movement and operation.

19. Cabin Decals, Labels, and Placards - inspect for presence	__________________

and legibility.

20. Upholstery, Headliner, Trim and Carpeting -  check	__________________

condition and clean as required.

21. Lighting, Fresh Air Vents - check condition and operation	__________________

of reading and courtesy lights and fresh air vents.

22. Windows, Windshield, and Seals - inspect general condition	__________________

Check latches, hinges, and seals for condition, operation and

security of attachment.  Check windshield for distortion and cracks.

CABIN	INSP.

23. Baggage Door (201 and Warrior only) - check latches, hinges,	__________________

and door strap for security and operation.

24. Cabin Doors - inspect hinges and latching mechanism for	__________________

proper operation, wear, and security.

- Fire Extinguisher - inspect fire extinguisher and attach bracket

for security and condition.  Inspect nozzle for obstructions and

ensure safety seal is intact.  Weigh fire extinguisher to ensure it

meets the weight requirement as printed on the extinguisher placard.

_____________________________________________________________________________

EMPENNAGE	    INSP.

1.	Vertical stabilizer - inspect externally for	__________________

skin damage, condition of paint and condition

of fairings and tip.  Check hinges and bolts

for condition and security.

2.	Rudder - inspect skin for condition, hinges for	__________________

condition and security.  Check travel stops.

3.	Tailcone - remove cone.  Inspect rudder horn and 	__________________

cables for condition and security of attachment.  Inspect

vertical stabilizer brackets and attach bolts for cracks,

corrosion and security of attachment.  Inspect stabilator spar

for cracks.  Install tailcone.

4.	Stabilator/Trim Tab - check skin for damage and security, tips	__________________

for cracks and condition.  Check hinges and bolts for security

and condition. Check balance weights for security and

attachment.  Check tab hinge for tightness and security and

tab linkage for excessive travel or play.  Inspect trim

actuator for security and operation.

5.	Empennage Internal Structure and Components - inspect	__________________

structure for evidence of damage or stress.  Check all

elevator, rudder and trim cables for proper tension,

and pulleys for freedom of movement,

alignment and security of turn-buckles and travel stops.

6.		Emergency Locator Transmitter - inspect for condition and	__________________

security of transmitter, cable and antenna.  Check battery

replacement date, check yearly inspection compliance date.

Check unit for proper operation and signal strength.

_____________________________________________________________________________

ROUTINE INSPECTION ITEMS---ENGINE, PROPELLER, WINGS, LANDING GEAR

ENGINE	    INSP.

1.		Cowling - check for condition and security.	__________________

2.		Air Filter - check condition, clean or replace as required.	__________________

3.		Ducting - check for condition and security, replace as required	__________________

4.		Oil Lines - inspect lines, fittings, fire shielding, and radiator	__________________

for leaks, condition and security.

5.		Fuel System - check pump, injector and lines for leakage,	__________________

condition and security.

6.	Fuel Screen & Sump - check fuel sump drain operation.	__________________

7.	Exhaust System - inspect gaskets, clamps, exhaust pipes and	__________________

heat exchanger externally for cracks, leaks and wear.

8.	Engine Baffles - inspect for condition and security.	__________________

9.	Engine Controls - check for proper attachment and travel.	__________________

10. Oil Filter and Sump Screen – Drain oil, internally inspect oil	__________________

filter element and replace with new filter.

11.	Oil – Fill with proper grade oil. 	__________________

12. Induction System - check security of clamps, tubes and 	__________________

ducting.  Inspect for evidence of leakage.

_______________________________________________________________________________

PROPELLER	    INSP.

1.	Propeller Blades - inspect for cracks, dents, nicks,	__________________

scratches, erosion, corrosion, or other damage.

2.	Spinner - check general condition and attachment.	__________________

_____________________________________________________________________________

WINGS    	    INSP.

1.	Wing Surfaces and Tips - inspect for skin damage,	__________________

condition of paint, and security of inspection covers,

fairings and tips.  Check condition and security of

navigation lights.

2.	Ailerons - check skin for condition and security.  Check	__________________

hinges, pins, attach points, brackets, balance weights, and

push-pull rods for condition and security.

3.	Flaps - check skin for condition and security.  Check	__________________

hinge attach points, bearings, bolts and push-pull rods

for condition and security.

4.	Fuel Drains - inspect for evidence of leakage, security,	__________________

drain water and sediment.

5.	Fuel Vents, Air Inlets, Pitot Tube, and Stall Warning	__________________

Vanes - check for condition and obstructions.  Check

pitot heater.

6.	Fuel Tanks - check for evidence of leakage and condition	__________________

of fuel caps and placards.

_______________________________________________________________________________

LANDING GEAR	    INSP.

1.	Actuator Cylinders (201 only) - inspect for leakage and	__________________

condition.  Check hoses for wear and abrasion.

2.	Retract Linkage, Wiring and Switches (201 only) - check	__________________

for security and proper alignment.

3.	Landing Gear Strut Assy (161 only) - check condition and	__________________

security.  Check upper and lower spar attach area for

deformation or looseness.

4.	Struts and Doors (201 only) - check condition and	__________________

security.  Determine that all clevis retaining pins are

in place and secured with cotter keys.  Check struts for

proper inflation.

5.	Wheels, Tires, and Brakes - check for condition, tires for	__________________

wear and inflation, and brake linings for wear.

_______________________________________________________________________________

POST INSPECTION	    INSP.

1.	Lubrication and Servicing - insure all required items	__________________

have been lubricated and serviced per appropriate

lubrication and servicing charts.

2.	Ensure all access covers, doors, fairings, and other items	__________________

removed for this inspection are reinstalled properly.

_______________________________________________________________________________

POST INSPECTION RUN-UP

1.  Brakes

2.  Starter

3.  Engine Instr.

4.  Alternator Output

5.  Avionics Oper.

6.  Ammeter

7.  Magneto-175 Max, 50

Diff at 2000 RPM Max

10 sec. each mag.

8.	Carb Heat Check

- Propeller check at 1500 RPM,

500 RPM decrease (201 only)

- Power Check (Max 2 min. or

475F with cowling removed)

- Heat and Vent

System

12.	Fuel Gauges

13.	Boost Pump

14.	Fuel Selector

15.	All Lights

16.	Electric Trim Oper.

17.	Flaps

18.	Pitot Heat

19.	Instruments

- Standby Vacuum Pump

21.	Idle RPM, 550-650 RPM

22.	Idle cut-off

23.	Magneto Safety Check

POST RUN-UP INSPECTION						INSP.

1.	Engine Compartment - check for oil and fuel leaks.			__________________

Reinstall Cowling.

2.	Aircraft Records - check for completion of Service			__________________

Bulletins, Airworthiness Directives, Maintenance

Record Entries.

_________________________________________________________________________

INSPECTION NO. 1 COMPLETED		DATE:

Early and Late Inspections 
The 60 hour inspection interval may be performed from 10 hours before the scheduled time to 10 hours after the scheduled time.  However, the due time for the next inspection is calculated using the original inspection time.  For example, say that the Phase 1 inspection is due at 660 hrs.  The inspection may be performed anytime from 650 hrs. to 670 hrs.  However, the Phase 2 inspection is due at 720 hrs. (60 hrs. after 660), regardless of when the Phase 1 was completed.

As the pilot, you still cannot over-fly the time listed on the “DO NOT OVERFLY--->” line on the aircraft inspection sheet.

Records 
Each inspection has its own inspection form that the mechanic or station completes. The completed form is kept until the next equivalent inspection is completed. The phase inspection is also recorded on the Permanent Aircraft Maintenance Record.

Special Inspections and Time Limited Items 
Several items on the aircraft have separate inspection periods or specified lifetimes (hour limits). The hour limits on these items may be exceeded by 60 hours to fall within a scheduled inspection period, unless the replacement is mandated by an AD. The items with separate inspection periods or hour limited lives appear below:

| Hour Interval | Items |
| --- | --- |
| 500 Hrs or 10 Yrs | Replace Auxiliary Vacuum Pump Inspect Internal Magneto and Impulse Coupling |
| 1000 Hrs | Replace Alternator Brushes Replace Exhaust Collector |
| At Engine Overhaul | Replace All Hoses, Rubber Engine Mounts, and Mount Bolts and Nuts Overhaul Propeller |
| Every 12 Cal. Mos. | Inspect ELT |
| Every 24 Cal. Mos. | Inspect Altimeter, Encoder, and Transponder Systems |

Maintenance Records 
UND maintains maintenance records in compliance with FAR Part 91. There are several records that UND keeps:

- UND Aerospace work orders serve as the permanent maintenance record under the progressive inspection program.

- A record of all work performed on the aircraft is included in the Aircraft Permanent Maintenance Record.

- Maintenance conducted away from the aircraft's base is recorded on the aircraft discrepancy sheet.

- Completed inspection forms are kept until the next equivalent inspection

- Status sheets are placed in the aircraft book (front page) and reflect the current status of inspections and airworthiness directives.

- These sheets state the tach times and dates of upcoming inspections.

- The “DO NOT OVERFLY” dates and times must be followed!

Preventative Maintenance

The FAR Part 43 lists approximately two dozen relatively uncomplicated repairs and procedures defined as preventative maintenance.

These include:

- Removal, installation, and repair of landing gear tires

- Replacing elastic shock absorber cords on landing gear

- Servicing landing gear shock struts by adding oil, air, or both

- Servicing landing gear wheel bearings

- Replacing defective safety wiring or cotter keys

- Lubrication not requiring disassembly other than removal of nonstructural items such as cover plates, cowlings, and fairings

- Making simple fabric patches

- Replenishing hydraulic fluid in the hydraulic reservoir

- Refinishing decorative coating of fuselage

- Applying preservative or protective material to components

- Repairing upholstery

- Making small simple repairs to fairings, nonstructural cover plates, cowlings, and small patches

- Replacing side windows where that work does not interfere with the structure

- Replacing safety belts

- Replacing seats

- Trouble shooting and repairing broken circuits in landing light wiring circuits

- Replacing bulbs, reflectors, and lenses of position and landing lights

- Replacing wheels and skis where no weight and balance computation is involved

- Replacing any cowling not requiring removal of the propeller or disconnection of  flight controls

- Replacing or cleaning spark plugs

- Replacing any hose connection

- Replacing prefabricated fuel lines

- Cleaning or replacing fuel and oil strainers

- Replacing and servicing batteries

Certificated pilots, excluding student pilots, may perform preventative maintenance on any aircraft owned or operated by them that are not used in air carrier service.

Repairs and Alterations

All repairs and alterations are classified as either major or minor.  Major repairs or major alterations must be approved for return to service by an appropriately rated certificated repair station, an FAA certificated A & P mechanic holding an Inspection Authorization, or a representative of the Administrator.  Minor repairs and alterations may be approved for return to service by an FAA certificated A & P mechanic or an appropriately certificated repair station.

Type Data Sheet

A Type Data Sheet prescribes conditions and limitations under which the product for which the type certificate was issued meets the airworthiness requirements for the Federal Aviation Regulations.

Here is the type data sheet for the Arrow taken from FAR Part 23.

Airworthiness Directives

A primary safety function of the FAA is to require correction of unsafe conditions found in an aircraft, aircraft engine, propeller, or appliance when such conditions exist or are likely to exist or develop in other products of the same design.  The unsafe conditions may exist because of a design defect, maintenance, or other causes.  FAR Part 39, Airworthiness Directives, defines the authority and responsibility of the Administrator for requiring the necessary corrective action.  AD’s are the media used to notify aircraft owners and other interested persons of unsafe conditions and to specify the conditions under which the product may continue to be operated.

AD’s may be divided into two categories:

- Those of an emergency nature requiring immediate compliance prior to further flight

- Those of a less urgent nature requiring compliance within a relatively longer period of time

AD’s are FAR’s and must be complied with, unless specific exemption is granted.  It is the aircraft owner’s or operator’s responsibility to assure compliance with all pertinent AD’s.  This includes those AD’s that require recurrent and continuing action.  For example, an AD may require a repetitive inspection each 50 hours of operation, meaning the particular inspection shall be accomplished and recorded every 50 hours of time in service.

FAR’s require a record to be maintained that shows the current s status of applicable AD’s, including the method of compliance, the AD number and revision date, and the signature and certificate number of the repair station or mechanic who performed the work.

Sample Airworthiness Directive for the Arrow’s fuel injector lines:

Service Bulletins

These are usually maintenance items which need to be addresses in which the manufacturer has found need attention.  These are not mandatory, according to the FARs, but may void any warranty or responsibility by the manufacturer.  Although, Piper does consider compliance mandatory.

Sample Service Bulletin for fuel line: